## Slide 1
AIR CONDITIONING · CHAPTER 1
1.4 Main Equipment in Air Conditioning Systems
Compressors, condensers, expansion devices, AHU and FCU
A visual-led lecture deck for concept-first teaching and engineering discussion.
Compressor
Condenser
Expansion
AHU/FCU
1.4
1
2
3
4
From components → decisions → engineering judgement
Air Conditioning · Chapter 1 · Topic 1.4
1

## Slide 2
Equipment follows the refrigeration loop
The four functions become real machines and devices.
2
Air Conditioning · Chapter 1 · Topic 1.4
2
EQUIPMENT MAP
Same physics, many equipment choices
1
Pressure rise
compressor family
2
Heat rejection
condenser type
3
Flow control
expansion device
Main equipment groups

## Slide 3
Compressor type depends strongly on capacity
Small units and large plants use different compression mechanisms.
3
Air Conditioning · Chapter 1 · Topic 1.4
3
COMPRESSOR SELECTION
Match technology to capacity and load profile
1
Reciprocating
small, simple, serviceable
2
Scroll
quiet residential/light commercial
3
Screw
medium-large, good part load
Compressor type capacity/application comparison

## Slide 4
Condenser choice changes system efficiency
Lower condensing temperature usually means higher COP.
4
Air Conditioning · Chapter 1 · Topic 1.4
4
HEAT REJECTION
Air-cooled vs water-cooled is an energy decision
1
Air-cooled
simple, no water system
2
Water-cooled
lower condensing temperature
3
Evaporative
approaches wet-bulb temperature
Condensing temperature comparison

## Slide 5
Expansion devices meter refrigerant into the evaporator
Control precision increases from capillary tube to EEV.
5
Air Conditioning · Chapter 1 · Topic 1.4
5
FLOW CONTROL
The valve protects superheat and capacity
1
Capillary tube
fixed, cheap, charge-sensitive
2
TXV
mechanical superheat control
3
EEV
fast, precise, inverter/VRF friendly
Expansion device comparison

## Slide 6
AHU and FCU solve different air-distribution problems
Centralized air handling versus room-by-room control.
6
Air Conditioning · Chapter 1 · Topic 1.4
6
AIR-SIDE EQUIPMENT
Choose distribution strategy by building use
1
AHU
large zones, ductwork, central filtration
2
FCU
individual zones, compact terminal unit
3
Fresh air
often handled centrally or by DOAS
AHU vs FCU strategies

## Slide 7
Topic 1.4 summary
What students should remember
7
Air Conditioning · Chapter 1 · Topic 1.4
7
1
Compressor sets capacity
select by size, load profile, and efficiency
2
Condenser sets heat rejection
water-cooled can raise COP but adds systems
3
Air-side choice affects operation
AHU for central zones; FCU for distributed control