## Slide 1
1.1 | Air Conditioning
Definition, Purpose, and Scope
occupied space
1
Air Conditioning · Chapter 1 · Topic 1.1

## Slide 2
Cooling alone is not air conditioning
Start with the misconception and correct it visually.
Air conditioning controls the indoor environment, not only air temperature.
Core idea: cooling is only one part of air conditioning.
2
Air Conditioning · Chapter 1 · Topic 1.1

## Slide 3
Four parameters must be controlled together
Use the 2×2 visual as the core definition.
Temperature — dry-bulb target
Humidity — relative humidity / latent load
Air circulation — air movement and distribution
Air cleanliness — filtration and contaminant control
3
Air Conditioning · Chapter 1 · Topic 1.1

## Slide 4
If one control fails, the whole environment can fail
A good temperature reading does not guarantee a good indoor environment.
Example: 25 °C but high humidity can still feel sticky.
Example: clean temperature control but poor ventilation can allow CO₂ or VOCs to accumulate.
4
Air Conditioning · Chapter 1 · Topic 1.1

## Slide 5
Purpose changes the design target
Comfort AC and process AC use the same variables for different goals.
Comfort AC: goal = human thermal comfort
Process AC: goal = product, material, or process requirement
5
Air Conditioning · Chapter 1 · Topic 1.1

## Slide 6
Comfort AC supports the body’s heat balance
Use the human body as the “sensor” for comfort air conditioning.
Convection
Radiation
Conduction
Evaporation
6
Air Conditioning · Chapter 1 · Topic 1.1

## Slide 7
Process AC may target conditions humans would not choose
Let the product/process define the control objective.
Textile mill: higher humidity to reduce static and thread breakage
Paper storage: lower humidity to prevent deformation
Seed storage: low temperature and humidity to preserve viability
7
Air Conditioning · Chapter 1 · Topic 1.1

## Slide 8
Equipment sizing is a peak-load problem
Capacity must match the maximum heat gain rate during operation.
Air conditioners are sized for the maximum expected load, not the average load.
8
Air Conditioning · Chapter 1 · Topic 1.1

## Slide 9
Office peak load often occurs after solar noon
Stored heat and internal gains shift the maximum into mid-afternoon.
Solar gain + envelope thermal lag + occupants + lighting + equipment
Typical office peak: around 15:00–16:00
9
Air Conditioning · Chapter 1 · Topic 1.1

## Slide 10
Nightclub peak load is driven by people and lighting
A building with little solar gain can peak at night.
Peak may occur around 21:00–22:00
Dominant loads: occupants, lighting, latent heat, and equipment
10
Air Conditioning · Chapter 1 · Topic 1.1

## Slide 11
A building survey turns assumptions into inputs
The survey is the first engineering step before load calculation.
Survey = measure + collect + verify project data
Good survey data reduce over-sizing, under-sizing, and design uncertainty.
11
Air Conditioning · Chapter 1 · Topic 1.1

## Slide 12
What must be surveyed?
Organize inputs into external and internal data.
External data: location, orientation, solar exposure, surrounding shading, outdoor unit location
Internal data: room size, occupancy, lighting, equipment, ventilation, operating schedule
12
Air Conditioning · Chapter 1 · Topic 1.1

## Slide 13
This course focuses on cooling-mode AC in Thailand
Scope the textbook/course so students know what is included and excluded.
Thailand context: high outdoor temperature + high humidity
Main needs: cooling and dehumidification
Heating and humidification are outside the main scope.
13
Air Conditioning · Chapter 1 · Topic 1.1

## Slide 14
Pause question: which parameter controls the problem?
Use this as an interactive slide before summarizing.
A classroom is 25 °C but students feel sticky. Which parameter is likely the problem?
Answer: humidity and/or air movement.
14
Air Conditioning · Chapter 1 · Topic 1.1

## Slide 15
Topic 1.1 — what students should remember
AC = simultaneous control of temperature + humidity + circulation + cleanliness
Comfort AC is for humans; process AC is for materials or production.
Building survey provides the inputs for load calculation and system selection.
15
Air Conditioning · Chapter 1 · Topic 1.1