## Slide 1
1.2 | Peak Cooling Load
Concept and Design Basis
1
peak
Air Conditioning · Chapter 1 · Topic 1.2

## Slide 2
A room warms up when heat enters faster than the system removes it
Use a simple balance: heat gain versus cooling capacity.
2
Heat gain raises the room load.
Cooling capacity must remove heat at the required rate.
Air Conditioning · Chapter 1 · Topic 1.2

## Slide 3
Peak cooling load is the maximum simultaneous heat gain
A daily profile converts a moving problem into one design hour.
3
The design point is the maximum expected load during operation.
Do not size equipment using only an average load.
Air Conditioning · Chapter 1 · Topic 1.2

## Slide 4
Total load is built from three families of heat gain
Use categories before equations.
4
External load: solar + envelope conduction + lag
Internal load: people + lighting + equipment
Outdoor air load: ventilation + infiltration
Air Conditioning · Chapter 1 · Topic 1.2

## Slide 5
Envelope heat gain can arrive hours after the sun hits the building
Thermal lag shifts the load peak into the afternoon.
5
Wall and roof mass store heat temporarily.
The indoor cooling load may peak after solar noon.
Air Conditioning · Chapter 1 · Topic 1.2

## Slide 6
Office buildings often peak at 15:00–16:00
West solar gain, thermal lag, and internal gains overlap.
6
Solar load + internal load + time lag create the peak period.
The peak hour depends on building use and orientation.
Air Conditioning · Chapter 1 · Topic 1.2

## Slide 7
A nightclub peaks at night because the use pattern changes the load
Peak time follows dominant heat sources.
7
Solar gain may be zero at night.
Occupants, lighting, latent heat, and equipment dominate.
Air Conditioning · Chapter 1 · Topic 1.2

## Slide 8
Wrong capacity creates two different failure modes
Both undersizing and oversizing are engineering mistakes.
8
Undersized: cannot hold setpoint at peak.
Oversized: short cycling, poor humidity control, and higher cost.
Air Conditioning · Chapter 1 · Topic 1.2

## Slide 9
Peak load calculation is a structured workflow
Before equipment selection, calculate the hourly total.
9
Survey → design conditions → load components → hourly total → equipment selection
Air Conditioning · Chapter 1 · Topic 1.2

## Slide 10
Quick check before moving on
10
Why is peak load not always at noon?
Which load component is most dependent on building use?
Why can oversizing be a problem?
Air Conditioning · Chapter 1 · Topic 1.2