## Slide 1
AIR CONDITIONING · CHAPTER 1
1.1 Air Conditioning
Definition, Purpose, and Scope
Air conditioning is not simply cooling. It is the simultaneous control of the indoor environment.
Temperature
Humidity
Air circulation
Air cleanliness
Teaching focus: cooling-mode AC for Thailand
Air Conditioning · Chapter 1 · Topic 1.1
1

## Slide 2
1.1 | Cooling only is not air conditioning
Start with the misconception and correct it visually.
Air Conditioning · Chapter 1 · Topic 1.1
2

## Slide 3
Four parameters must be controlled together
Use the 2×2 visual as the core definition.
3
Air Conditioning · Chapter 1 · Topic 1.1
3
CORE DEFINITION
Control these together
1
Temperature
sensible heat balance
2
Humidity
latent moisture control
3
Air circulation
mixing + distribution
4
Air cleanliness
filtration + dilution

## Slide 4
If one control fails, the whole environment can fail
A good temperature reading does not guarantee a good indoor environment.
4
Air Conditioning · Chapter 1 · Topic 1.1
4
WHY IT MATTERS
One weak control can ruin comfort
1
Sticky at 25 °C
humidity is still too high
2
Stale or smelly air
ventilation/cleanliness is weak
3
Uneven room comfort
poor air distribution

## Slide 5
Purpose changes the design target
Comfort AC and process AC use the same variables for different goals.
5
Air Conditioning · Chapter 1 · Topic 1.1
5
DESIGN TARGET
Purpose changes the setpoint
1
Comfort AC
human thermal comfort
2
Process AC
product, material, or process requirement

## Slide 6
Comfort AC supports the body’s heat balance
Use the human body as the “sensor” for comfort air conditioning.
6
Air Conditioning · Chapter 1 · Topic 1.1
6
COMFORT MECHANISMS
The body is the sensor
1
Convection
heat transfer to moving air
2
Radiation
exchange with surfaces
3
Conduction
contact with materials
4
Evaporation
sweat + moisture removal

## Slide 7
Process AC may target conditions humans would not choose
Let the product/process define the control objective.
7
Air Conditioning · Chapter 1 · Topic 1.1
7
PROCESS EXAMPLES
The product defines comfort
1
Textile mill
higher RH for fibers
2
Paper storage
lower RH to protect stock
3
Seed storage
low temperature + low humidity

## Slide 8
Equipment sizing is a peak-load problem
Capacity must match the maximum heat gain rate during operation.
8
Air Conditioning · Chapter 1 · Topic 1.1
8
Peak
Avg
Time of day →
SIZING PRINCIPLE
Peak load sets capacity
Design for maximum expected load
not the daily average
Average load can be misleading
capacity may be undersized

## Slide 9
Office peak load often occurs after solar noon
Stored heat and internal gains shift the maximum into mid-afternoon.
9
Air Conditioning · Chapter 1 · Topic 1.1
9
Load
08:00
12:00
16:00
20:00
Peak around 15:00–16:00
solar + thermal lag + internal gains
Peak follows use pattern

## Slide 10
Nightclub peak load is driven by people and lighting
A building with little solar gain can peak at night.
10
Air Conditioning · Chapter 1 · Topic 1.1
10
Load
18:00
20:00
22:00
24:00
Peak around 21:00–22:00
occupants + lighting + latent heat
Peak follows use pattern

## Slide 11
A building survey turns assumptions into inputs
The survey is the first engineering step before load calculation.
11
Air Conditioning · Chapter 1 · Topic 1.1
11
FIRST ENGINEERING STEP
Survey before calculating
1
Measure
room size and envelope data
2
Collect
loads, schedules, ventilation needs
3
Verify
reduce over/under-sizing risk

## Slide 12
What must be surveyed?
Organize inputs into external and internal data.
12
Air Conditioning · Chapter 1 · Topic 1.1
12
SURVEY CHECKLIST
External + internal inputs
1
External data
location, orientation, solar exposure, shading
2
Internal data
room size, occupancy, lighting, equipment, schedule

## Slide 13
This course focuses on cooling-mode AC in Thailand
Scope the course so students know what is included and excluded.
13
Air Conditioning · Chapter 1 · Topic 1.1
13
Thailand design context
☀
High outdoor temperature
sensible load
RH
High humidity
latent load
AC
Cooling + dehumidification
main course scope
Heating and humidification are not the main focus for this course.

## Slide 14
Pause question: which parameter controls the problem?
Use this as an interactive slide before summarizing.
14
Air Conditioning · Chapter 1 · Topic 1.1
14
A classroom is 25 °C, but students feel sticky.
Which parameter is likely the problem?
Temperature
Humidity
Air motion
Cleanliness
Expected answer: humidity and/or air movement.

## Slide 15
Topic 1.1 — what students should remember
15
Air Conditioning · Chapter 1 · Topic 1.1
15
1
AC = simultaneous control
Temperature + humidity + circulation + cleanliness
2
Purpose defines target
Comfort for people or process conditions for materials
3
Survey before design
Survey data become load-calculation inputs